* Medusa
* Ncrack
* Hydra

* Can use Crunch and save pwd list then pass to John the Ripper though john does not need a file and can do password cracking on its own.

## Password Locations
- Linux - /etc/shadow
- Windows SAM – C:\Windows\System32\config\sam
- Windows Domain Controller - C:\WindowsNT\dsn\ntds.dit
## Dictionary Attack
- Uses normal words found in a dictionary such as “John”, “Jane”, etc.
- Store the hash of each word in a file and compare to stolen pwds.
- rockyou.txt
## Rainbow Table Attack
https://freerainbowtables.com/
- Trade-off between bruit force and dictionary.
  - Uses more memory of bruit force (but less CPU).
  - Uses more CPU than dictionary (but less storage).
- rtgen – tool used to generate a rainbow table.
- Each row in the table is a “chain” and each column is length of each chain.
- Specific to the hash function used to create the Table. MD5 tables can only crack MD5 hashes.
- Uses a Reduction Function to map hashed into something that could be a pwd.
  - Uses a different reduction function for each chain link so that when there is a hash collision in two or more chains, the chains won’t merge, as long as the collision does not occur in the same location of each chain.
  - Using multiple reduction function increases the probability of a correct crack for a given table size.
  - Also using multiples almost doubles the speed of lookups.
- Alternating hashing and reducing to produce a chain of alternating hashes and plain text.
- Dave (hash ->) 12345 (reduction function ->) SomeText (hash → ) 88997
- Compute a number of chains with a specific length.
  - Instead of storing 10,000 plain-text values (which can crack 10,000 pwds), only store the beginning and end point of 5,000 chains.
  - *** This can crack any number of pwds, 100,000, 1M, 1B, etc.
## Salt
Renders Rainbow tables useless.